## Slide 1: Supergrid Modelling for the Indian Subcontinent
Farhan Beg
Global Energy Network Institute
With Inputs from Mr. Peter Meissen and Mr. Paul Michael Dekker

## Slide 2: Supergrid
High Voltage Energy Corridor that is based on an HVDC transmission network
Carries large quantities of power across long distances and between countries
Capability of integrating renewable energy into the grids

## Slide 3
The European Supergrid
Source: www.earthtimes.org
European Supergrid with proposed renewable integration from Northern Africa consisting of a meshed grid structure

## Slide 4: Scope of the Supergrid Deployment
Large Renewable Energy Potential is located in the Indian Subcontinent
  Not in Immediate Proximity to Load centers
Strong need to integrate the renewable energy into existing electricity grid
  Curb the energy shortages
  Improve quality of electricity
  Regulate the price of electricity

## Slide 5: Energy Transfer from Generation to Demand Locations
Positive Energy Gradient from east to west
Positive Load Gradient from west to east
Cluster of load centers
Cluster of generation centers
[Farhan Beg 2014]

## Slide 6: What will it look like?
[Farhan Beg 2014]
The proposed draft model of the Supergrid for the Indian subcontinent

## Slide 7: Need based Assessment of the Member Countries
Scale and complexity of the project
Huge variation of economic and cultural trends across the subcontinent
Individual member countries’ needs have to be respected

## Slide 8: Energy Assessment of India
Shortage of coal at Coal based generating plants
Refining and extraction of Coal does not match the coal utilization factor of the plants
Import of Gas not a feasible option.
Renewable energy resources far from the load centers.
Chart: 
| Coal | Diesel | Gas | Hydro | Nuclear | Non renewables
 | 120783 | 1200 | 18903 | 39324 | 4780 | 25856
Figure: Electricity Generation from different sources (2011) [Farhan Beg 2014]

## Slide 9: Energy Assessment of Pakistan
Electricity supply is highly unreliable.
Load shedding and power outages are a common scene every day.
Energy shortages at generating stations
Chart: 
| Fossil Fuels | Nuclear Fuels | Hydro power | Renewable
Sales | 64.3 | 2.3 | 32.5 | 0.9
Figure: Electricity Generation from different sources (2011) [Farhan Beg 2014]

## Slide 10: Pakistan’s Supply/Demand Inconsistency
Source: EIA Annual Report, Energy trends
Pakistan’s supply side has seen no growth over the years with the demand increasing consistently

## Slide 11: Location of Sindh Valley
Total Wind Potential of Pakistan is 150 GW
Wind Potential of the Sindh Valley is 50 GW
[Farhan Beg 2014]
Sindh valley has been identified as a potential Wind Energy source for integration into the supergrid for the power flow analysis

## Slide 12: Pakistan Wind Resources

## Slide 13: Energy Assessment of Bhutan
As of 2012, only about 70% of households had access to electricity
Hydro power potential of around 30GW
Exports more than 75% of hydroelectricity to India
Developmental goals based on foreign exchange from the export of hydro power.
Source: www.nrel.gov
Figure: Bhutan Total Electricity Exports Source: www.tudorancea.com

## Slide 14: Energy Assessment of Bangladesh
Source: wikipedia.org/bangladeshelectricity
Source: Wikipedia.org/bangladesh
Figure: Bangladesh location

## Slide 15
Chart: 
| 2000 | 2002 | 2004 | 2006 | 2008 | 2012
MW | 4000 | 4400 | 4600 | 5200 | 5800 | 6600
Growth Rate of 6.6%
Electricity capacity will be nearly 10,000 MW by 2020, which is far from the estimated demand of 15000 MW.
Electricity Generation Capacity of Bangladesh
[Farhan Beg 2014]

## Slide 16: Energy Assessment of Sri Lanka
Sri Lanka has total identified hydro power potential of 2GW out of which nearly 1.5GW has already been harnessed
Energy demand will outpace energy generated in Sri Lanka in the next 20 years.
Source: www.wikipedia.org/srilanka

## Slide 17: Energy Assessment of Nepal
Overall fuel wood supplies nearly 80% of energy consumption.
Total potential of electricity generation about 83GW
Potential tapped 0.28GW
40% of households have access to electricity
Source: energy4livelihood.com

## Slide 18: Country-wise Potential/Tapped
Chart: 
| India | Pakistan | Bangladesh | Bhutan | Nepal | SriLanka
Estimated in MW | 102000 | 150000 | 755 | 23670 | 32000 | 2000
Developed in MW | 20000 | 2500 | 218 | 469 | 613.5 | 1500
755
218
[Farhan Beg 2014]

## Slide 19: Supergrid Modelling
Provide an electricity highway for the flow of electric power between nations
Provide a capability to interconnect the asynchronous transmission systems of the subcontinent
Efficiently control the exchange of seasonally varying production and storage capacities.

## Slide 20: State of Technology
Three-Phase AC technology 50 Hz (AC grids) with voltages >400 kV (750 kV, 1000 kV)
Three-Phase AC technology with reduced frequency (AC grids 16 2/3 Hz) with voltages >400 kV
High Voltage Direct Current Transmission
P=**()
2**
Power transfer equation

## Slide 21: Increase in Transmission Voltage Levels
Synchronous System Connections
Asynchronous System Connections
Source: PowerGrid Corporation of India Limited

## Slide 22: Multi Terminal DC Connections
Two choices of connections
Series
Parallel
Figure: Parallel multi terminal DC connections for the Supergrid.
Generator
Transmission Line
Converter Station
[Farhan Beg 2014]

## Slide 23: Power Flow Analysis
A tool to obtain the best working conditions for an interconnected system.
Conditions are obtained by solving the voltage and current balance equations at the nodes.
For DC network the power flow is simpler.
[Farhan Beg 2014]

## Slide 24: Draft Model of the Supergrid
{Farhan Beg 2014}

## Slide 25
Supergrid Modelling
[Farhan Beg 2014]
AC/DC Buses

## Slide 26
For any inquiries, please contact the author at farhan.beg@geni.org
Farhan Beg is a power engineer from the National Institute of Technology, Srinagar, India and is a researcher at the Global Energy Network Institute, San Diego, CA, USA
This is an ongoing research project at the Global Energy Network Institute, San Diego, CA, USA
For a detailed analysis of the supergrid modelling and the technical concepts please visit the report “Supergrid Modelling and Risk Assessment for the Indian Subcontinent” at www.geni.org